## Slide 1: Temperature Screening and Considerations for Thermometers
Master training program
[Date]
Notes: This section describes an important part of conducting a risk assessment of an ill traveler – taking temperatures.

## Slide 2: Learning Objectives
Determine the role of temperature screening in health surveillance
Discuss the primary methods of temperature screening at a POE
Learn the primary considerations for thermal scanners (if used) at a POE
Notes: Our first objective for is to learn why temperature screening, or assessment, is so important in health surveillance at POE.
We’ll then get into the methods of taking a temperature at POE, and we’ll all get to practice and be evaluated on that activity.
Finally, we’ll have a brief discussion on the considerations for thermal scanners or body scanners, equipment which is becoming more and more common.

## Slide 3: Fever
Average body temperature is 37ºC
Fever is a measured body temperature above normal
  Fever is the most common symptom of an infectious disease
  Other causes of fever include other medical conditions, severe trauma or injury, or some medicines
Notes: So what is fever? It’s just a measured body temperature above the normal, which is 37 degrees Celsius.
Fever is the most common sign of infectious disease. In fact, can anyone raise their hand and share an infectious disease that has fever as a sign? Allow class to raise hands. Expected responses: measles, meningitis, Ebola/viral hemorrhagic fevers, etc. We will discuss clinical diagnostic criteria tomorrow, but remember that for the vast majority of infectious diseases, fever is a sign.
With that said, there are other conditions outside of infectious diseases that could still cause fever. Other medical conditions, severe trauma that your body is fighting—hence the fever—or even some medications can cause your fever to rise.

## Slide 4: Temperature Screening’s Role in Health Surveillance
It is routinely used at POE during ill traveler risk assessments
Always take a temperature during a risk assessment
It can be used at POE during disease-specific screening
Example photo; update with country-specific photo
Notes: Temperature assessment is common at POE and it is part of your role as [POE health agency] to do so during ill person risk assessments. Every time you get referred an ill passenger, you take a temperature. No questions asked. It is easy to do with the materials available to you.
Every now and then, the country may ask the POE to conduct temperature screening, which is usually the result of a local outbreak or, less frequently, WHO telling us to via a Public Health Emergency of International Concern declaration. When that occurs, you are charged to take temperatures of a greater amount of people. Usually, in these situations, there is specific guidance for this procedure.

## Slide 5: Temperature Screening is only Part of a Risk Assessment
Even the best temperature screening will still “miss” some infectious disease cases
  Travelers may be taking medications to mask their fever
  Travelers may have been infected with the disease but are not showing symptoms yet (i.e., are incubating disease)
  Some infections might not always have a fever, even when symptomatic, e.g., influenza
Temperature screening should be a necessary part, but not the only part, of a health risk assessment
  Also take medical history, travel history, symptom history, and exposure history
Notes: Before we get into the specifics of taking a temperature, I want to stress that it is a necessary part, but not the entirety of the ill passenger risk assessment process. Some people may be infected with a disease, but are not showing a fever. Why? Well, some could try to mask it by using paracetamol or other medications. Others may have already been exposed to disease and are infected with the disease, but may not be showing symptoms yet. This is known as “incubating” disease.
Different diseases behave differently in respect to fever and symptoms. One disease that is well known for being infectious while someone is incubating, or not yet showing symptoms, is influenza. However, Ebola can only be spread when someone is symptomatic.
Understanding these limitations, it is important to collect other information from people during risk assessments, like their past medical history, travel history, and exposure history. Temperature is only one part of the complete puzzle.

## Slide 6: Overview of thermometers
Thermometer (thermos: hot; metron: measure) is the universal instrument used to measure temperature
The ability to accurately find out if someone has a fever gives you much-needed information about important next steps for their care
There are many types of contact and contact-free thermometers
No matter which type you choose, read the manufacturer’s instructions carefully
No thermometer will provide accurate results if it’s used incorrectly
Notes: Like any other device in your home, it’s important to understand how your thermometer works. Not every type works the same way or is designed to provide the same temperature readings.
No matter which type you choose, read the manufacturer’s instructions carefully. No thermometer will provide accurate results if it’s used incorrectly.
Digital thermometers work by using heat sensors that determine body temperature. They can be used to take temperature readings in the mouth, rectum, or armpit. When assessing digital thermometer readings, keep in mind that armpit (axillary) temperature runs about ½ to 1°F (0.6°C) cooler than oral readings. Rectal thermometers run ½ to 1°F (0.6°C) warmer than oral readings.
Oral readings won’t be accurate if they are taken too close to eating or drinking, because results may be skewed by your food or drink’s temperature. Wait at least 15 minutes. Batteries in thermometers should be replaced periodically. Make sure you have the right type of batteries on hand for your device and that you understand how to change them, so you’re not left scrambling in an emergency.
Forehead thermometers use infrared sensors to measure the temperature of the superficial temporal artery, which is a branch of the carotid artery.
Some are known as non-contact infrared thermometers. Non-contact infrared thermometers are held three to 15 cm away from the patient and typically measure temperature on the forehead or temple. Forehead thermometers that require no physical contact have become very popular for use in venues such as airports, stores, and stadiums. Forehead thermometers must be positioned accurately and according to the manufacturer’s instructions, or they will not provide the right reading. Readings can be affected by external factors, including drafts, wind, indoor heating, and direct sunlight.
Wearing certain clothing, such as hats or heavy coats, can skew the results.

## Slide 7: Overview of Non-Contact Thermometers
A way to take someone’s temperature without touching them
Similar in accuracy to contact-based thermometers
Knowledge of specific model of non-contact thermometer is very important
  Calibration techniques
  Where to measure temperature
Example photos; update with country-specific photos
Notes: Now, all of you should have access to a non-contact thermometer at your POE. Is that correct? Allow for responses.
Thus, you should be aware of their benefits! They are a great way to take someone’s temperature without touching them, so this is very helpful for infection control purposes. They are similar in accuracy to contact-based thermometers without the cleanup and infection risk involved.
The main aspect you need to know about these thermometers is their model. There are many different types of non-contact thermometers, and each has slightly different ways of taking the temperature. For instance, some require that you take the temperature at the side of your head, and others require that you take it at the front of your head—look at the photos here for an example. Different models also differ in their calibration techniques, or the way you get the thermometer ready to take a temperature.

## Slide 8: Temperature “Cutoffs”
When you are not sure of the disease in question, usually a temperature of approximately 37.5ºC or 38ºC or higher is an indication that the person is ill
A person can still be infectious with a lower temperature – this is why other information is so important to collect
Temperature “cutoffs” are more useful during mass screening events like Ebola screening during the 2014-2015 West African outbreak
If a temperature if below 35ºC, retake the temperature
Temperature cutoff guidance during Ebola outbreak screening; update using country-specific cutoffs
Notes: We also wanted to give a quick note on temperature cutoffs. This is more useful during mass screening events like the Ebola outbreak than during routine times, but, if a person has a temperature beyond 37.5°C or 38°C, they can be sick and infectious. Even if they have a temperature below that level, they can still be sick and infectious, and this is again is reason to collect additional information like travel history, medical history, and exposure history.
However, if someone has a measured temperature below 35°C, measure it again. Most of us in this room would be dead if our temperatures were measured below 35 degrees! This also might be a sign that your thermometers needs to be re-calibrated or needs new batteries.

## Slide 9: Thermal Camera / Thermal Scanner Considerations
More common at airports than other POE
Advantages
  Can measure temperature from greater distance than a non-contact thermometer
  Can “screen” people faster vs. non-contact thermometers
Disadvantages
  Expensive
  Less accurate than non-contact thermometer - verify with a non-contact thermometer
  Considerable time for set-up and calibration
  Require more training of staff
Notes: Before we get into practicing measuring temperature, it’s important to quickly discuss thermal cameras, or as you sometimes hear them called, thermal scanners.
These are much more common at airports than at other POE, but they are quickly becoming quite common. Let’s discuss what they can and what they cannot do.
The advantage to these devices are that they can measure temperature from a greater distance than a non-contact thermometer. They also have the ability to screen people much quicker than a non-contact thermometer.
But you need to know their disadvantages. First and foremost, they are not as accurate as a non-contact thermometer. They have not been evaluated to be a primary diagnostic tool for any disease, and while you may be able to get an idea of fever from them, do not rely on them alone. Thus, if someone sets off the thermal camera or scanner with a fever that is above a pre-set threshold, most likely 37.5°C or 38°C, verify that temperature with a non-contact thermometer, which is more accurate.
Beyond this disadvantage, thermal cameras also must be highly calibrated and regularly maintained

## Slide 10: Non-Contact Thermometer Demonstration
By two facilitators
To read aloud thermometer calibration and temperature taking guidelines
Example photo; update with country-specific photo
Notes: Let’s now re-familiarize ourselves with taking a temperature properly. Ask 2 additional facilitators to come to the front of the room to assist. Also ask videographer to come back to the front of the room to take short videos.
We are going to demonstrate the process of taking a temperature. First, our facilitator/demonstrator is looking at the thermometer to ensure it has batteries and is ready for use. Pause to allow demonstrator to view thermometer and review batteries. Now, we need to ensure this thermometer is calibrated according to the instructions.
Allow the demonstrator to read aloud the calibration instructions for this particular thermometer, and have them act out the steps while reading.
Now that the thermometer is calibrated, it is ready for use. Remember to look back at the specific directions for this thermometer to see if you are measuring temperature at the front of the head or the side of the head. Ask the demonstrator to read aloud the instructions on where to take the temperature.
Now, we need to know how far back to stand to take a temperature. Ask the demonstrator to read aloud the instructions on how far back to stand to take the temperature.
Demonstrator takes the temperature and reads aloud to the class the answer. If it is below 35°C, they announce that the thermometer must be calibrated improperly or something must have happened and they take the temperature again. If is between 35-37.5°C, that is fine. If it is above 37.5°C, they want to ask the person additional questions, as they may be sick.

## Slide 11: Advantages and Disadvantages of Contact less Thermometers
Advantages | Disadvantages
Measurements can be taken from a distance where items should not be touched or contaminated. They are excellent for surface measurements Measurements can also be taken of moving parts Infrared thermometers operate well for a variety of applications Memory and advanced measurement functionality is available They are compact, lightweight, and easy to use | Infrared thermometers cannot take measurements of gas or liquids The environment needs to be clean, without dust, high humidity, or similar Depending on the model, the accuracy can be marginal Specialty meters can be very expensive
Notes: The following are the advantages and disadvantages of contactless thermometer usually refer to as infra red thermometer: Ask one of the participants to read the advantages and another read disadvantages.

## Slide 12: How to take temperature with a contactless forehead thermometer
Activate the device with the power button. You’ll know it’s on if it lights up and a startup sequence loads.
When your thermometer is ready, position it no more than 2 inches away from the center of the forehead. You can also touch the forehead with some models. Either way, you’ll get the most accurate reading possible if the forehead is clean and clear of hair.
Many thermometers have a guidance light that takes the guesswork out of positioning.
Make sure to hold the thermometer steady. The thermometer and forehead must be free of movement in order to get an accurate reading.
Press the temperature button.
Your device will beep or flash to let you know the temperature is ready to be read. This will only take around 2 seconds.
Notes: No-touch forehead thermometers usually have a removable cap that keeps it clean during storage. Make sure you take the cap off before use.

## Slide 13: Activity in Groups: Taking Temperatures
Break back into your groups
Each group will have a facilitator assigned to them
The facilitator will again demonstrate the accurate way of calibrating and taking a temperature; each group member has a chance to practice
Group members will then be evaluated in accurate temperature taking methods
Notes: Now for our activity! We’ll break into our groups again and each group will have a facilitator assigned to them.
Within the group, your facilitator will again demonstrate the process of taking a temperature. You then can have a chance to practice, without being graded, in taking temperatures. After practicing, each group member then will be evaluated on:
-Accurately turning on the thermometer and waiting until it was properly calibrated to take temperature. This includes checking the batteries.
-Taking temperature in the accurate location on the head
-Standing back in the appropriate location and not right next to the person (e.g. extending arm) for infection control purposes
-Reading out the temperature and then accurately interpreting the temperature (e.g. if below 35°C retaking, if 35-37.5°C okay, if past 37.5°C referred or asked for additional health surveillance measures)
Instruct participants to break into groups and follow the facilitators to certain areas of the room. Facilitator then demonstrates the use of the thermometer and allows each participant to practice—without grading—and offers recommendations for refinements and improvements. Each participant gets to practice once.
Then the facilitator needs to use the Temp Taking Evaluation Checklist to evaluate each of the participants.